## Slide 1: CSC Local Reconstruction Improvements Vladimir Palichik, Nikolay Voytishin JINR(Dubna)
JINR CMS Physics Meeting
December 14, 2017

## Slide 2: RU CSC Segment Builder
1000 GeV

## Slide 3: Event Example for R-coordinate
ST segments Goal segments
Collisions 2012 Run 198210 ME1/3 n_ev 1543
Collisions 2012 Run 198210 ME1/3 n_ev 12044

## Slide 4: Modified ST algo
Spanning Tree (ST)
(1)
(2)
Modified Spanning Tree (newST)
While adding hits on the next layer use lower_bound and upper_bound cuts in order for the segment to point towards the interaction point.
(3)
𝑢𝑝𝑝𝑒𝑟_𝑏𝑜𝑢𝑛𝑑= 𝑞𝑊𝐺_𝑚𝑎𝑥+1.5∗max𝑊𝐺_𝑤𝑖𝑑𝑡ℎ
𝑙𝑜𝑤𝑒𝑟_𝑏𝑜𝑢𝑛𝑑= 𝑞𝑊𝐺_𝑚𝑖𝑛−1.5∗max𝑊𝐺_𝑤𝑖dtℎ

## Slide 5: Segment Efficiency
Seg_efficiency =
Chart: 
| ST | new_ST | BaseRoad | BaseRoad+Baseline
10GeV | 85.83 | 91.42 | 93.16 | 92.77
100GeV | 81.63 | 88.15 | 91.15 | 90.42
1000GeV | 69.86 | 76.44 | 81.96 | 80.96

## Slide 6: RU(RoadUsage) Algorithm main ideas
Taking into account the IP while choosing the base hits in terms of WG for the future segment;
Base Road for RecHit association:
  A straight line is traced through the base hits
  In the road formed along this line new hits from the inner layers are added to the segment
Phi & tuned thresholds for each CSC station;
Optimal point rejection for bad segments.
  min()

## Slide 7
Additional tuning of the RU Algorithm
Increase dPhi threshold for base RecHits with big strip error;
Increase dPhi threshold for RecHits from inner layers reconstructed on the center of the strip or with big strip error;
Skip chamber with >150 RecHits;
Do not take as a base layer if there are >25 RecHits on this layer;
Build all possible same size proto-segments allowing RecHit overcrossing and choose best segments by criteria;
If there are enough unused RecHits left the segment reconstruction is run again with the IP check turned off in order to reconstruct segments that correspond to displaced muons.

## Slide 8: New algorithm promotion
A specialized validation code made for MC data analysis;
TnP analyzer modified for collisions analysis;
Multiple data analyzed:
  Private MC:
    Single Muon Pt10GeV;
    Single Muon Pt100GeV;
    Single Muon Pt1000GeV;
  MC RelVals:
    ZpMM;
    ZMM;
    ZMM+PU(25ns);
    ZMM+PU(50ns);
    TTBar;
  Collisions data (with various cuts on muon Pt):
    2012 collisions;
    2015 collisions;
    2016 collisions.
    Displaced Muons;
    Halo Muons;
    JPsi;
    Single Muon Pt1000GeV;
14 talks given on different meetings (CSC Weekly, MuPOG, RECO/AT) showing the comparison results and progress status of the new algorithm.

## Slide 9: Segment multiplicity per station
10 GeV
1000 GeV
100 GeV
ZMM+PU(25ns)
blue – ST algorithm; red – RU algorithm.

## Slide 10: Number of RecHits in all reconstructed segments
10 GeV
1000 GeV
ZMM+PU(25ns)
100 GeV
blue – ST algorithm; red – RU algorithm.

## Slide 11: RecHit efficiency vs η for muon segment
10 GeV
1000 GeV
100 GeV
ZMM+PU(25)
blue – ST algorithm; red – NEW algorithm.

## Slide 12: dPhi (RecoSeg - SimSeg)
10 GeV
1000 GeV
100 GeV
ZMM+PU(25)
blue – ST algorithm; red – RU algorithm.

## Slide 13: Collision data cut p>100GeV
100 GeV
SingleMuPt1000
Halo Muons
DisplacedMu SUSY
blue – ST algorithm; red – NEW algorithm.
blue – ST algorithm; red – NEW algorithm.
dPhi (Matched segment – GlobMu trajectory)
dTheta (Matched segment – GlobMu trajectory)

## Slide 14: High multiplicity example - 84 RecHits in Chamber
ST
15 segments
RU
4 segments
Muon trajectory

## Slide 15: High multiplicity example - 72 RecHits in ME21
Standard
10 segments
New
11 segments
Collisions2015 256630:26:34248876
Muon trajectory

## Slide 16: Pull Request submitted
https://github.com/cms-sw/cmssw/pull/14718 - June 20, 2016
After RECO conveners reviewed the code some modification and optimization to the code done;
PR got approved and RU builder became the 5th optional algorithm starting with Summer 2016;
Starting with 2017 data RU segment builder became the default builder for data and simulation reconstruction.

## Slide 17: Further issues
Minor bugs found by Marcello Maggi while adopting the RU segment builder for ME0 reconstruction – fixed;
Some improvement of the algorithm done – included in the update along with the fix from the previous bullet;
Multithreading issue due to improper initialization of some parameters (in progress), but a temporary fix already applied by Slava Krutelyov;

## Slide 18: RU algo used for GEM detectors in CMS
Reported by R. Venditti On Behalf of the CMS GEM Reco&Val group

## Slide 19: RH efficiency vs. attenuation factor with GIF++ data
blue – ST algorithm; red – RU algorithm.
RU algorithm in HL-LHC conditions
I ~ < I (HL-LHC) >
I ~ < I (HL-LHC) >

## Slide 20: Summary I
The new algorithm shows a better performance for all types of CMS data;
The optimization and bug elimination is continuously ongoing;
The RU algorithm was implemented in the official CMS software starting with CMSSW_8_1_0 (July, 2017);
The RU algorithm most probably will be used for segment reconstruction in the new GEM detectors of the CMS muon system;
The RU algorithm became the default segment reconstruction algorithm starting with CMSSW_9_X_X for Monte-Carlo production and experimental data reconstruction after the restart of LHC;
Using GIF++ data we showed that the new algorithm is less sensitive to HL-LHC conditions than the ST algorithm.

## Slide 21: CSC RecHit Reconstruction Improvement

## Slide 22: Why the improvement is needed ?
Additional options added to RU segment builder for handling “bad” RecHits (see talk [1]):
Increase dPhi threshold for base RecHits with big strip error;
Increase dPhi threshold for RecHits from inner layers reconstructed on the center of the strip or with big strip error;
Muon trajectory
Big strip error RHs
[1] https://indico.cern.ch/event/388966/contributions/922281/attachments/777650/1066373/15_04_22-Voytishin_Palichik-CSCSegBuilder_fixed_sumw.pdf
Regular strip charge distribution
~ 2% of strip width
Abnormal strip charge distributions
> 30% of strip width
Collisions 2015 event display

## Slide 23: When the improvement is needed ?
If > =>
the coordinate is calculated using Center of Gravity (CoG) like algorithm
Strip_nr*10
reconstructed coordinate
Charge on strips

## Slide 24: Introduction to wavelet analysis
The g2-WTS(Wavelet-TranSform method based on the usage of second degree wavelets ())[1] was chosen by us for overlapping signal recognition.
The main function in wavelet analysis is the following double gaussian function
(1)
While processing the signal it is divided in a set {}, where
= (2)
Gauss wavelets W for the function G can be represented as follows:
(3)
where
Here b is the shift, a is the scale and , – gaussian wavelet of the n-th degree, h- cluster of strip charges,- half-width of the wavelet.
To find the n-th wavelet coefficients of the set h we use:
(4)
G.Ososkov, A.Shitov Gaussian Wavelet Features and Their Applications for Analysis of Discretized Signals // Comp.Phys.Comm, v.126/1-2, 149-157, (2000)

## Slide 25: Our case
We build 2, 3 or 4 gaussians on a chosen interval of strips with a constant step. For the case of three overlapped signals the formula (1) looks as follows:
.
The parameters of the overlapped signals are obtained by summation of the values of these gaussians in each coordinate x.

## Slide 26: What has been done ?
Universal tool for overlapping signal recognition
Input data – ADCs on strips
Visualization of the input data
Result display
Search area selection
Strip_nr*10
Strip_nr
Strip_nr
ADCs
ADCs
Time Bins

## Slide 27: Good case example
The coordinate is well reconstructed by both methods (all coord’s coincide):
Yellow line – initial charge distribution;
Green line – simulated muon coordinate;
Red line – wavelet analysis;
Blue line – standard approach (Gatti fit).
~ 2% of strip width
NO need for improvement
Strip_nr*10
ADCs

## Slide 28: Two overlapped signals recognition
Yellow line – initial charge distribution;
Green line – simulated muon coordinate;
Red line – wavelet analysis;
Blue line – standard approach (CoG like).
> 25% of strip width
Strip_nr*10
ADCs

## Slide 29: Three overlapped signals recognition
Yellow line – initial charge distribution;
Green line – simulated muon coordinate;
Red line – wavelet analysis;
Blue line – standard approach (CoG like).
Strip_nr*10
ADCs
> 25% of strip width

## Slide 30: Four overlapped signals recognition
Yellow line – initial charge distribution;
Green line – simulated muon coordinate;
Red line – wavelet analysis;
Blue line – standard approach (CoG like).
Strip_nr*10
ADCs
> 25% of strip width

## Slide 31: dPhi (sim- reco)
Preliminary results
On MC Pt1000GeV

## Slide 32: Summary and plans
The development of the new RecHit reconstruction algorithm is ongoing;
The new approach reconstructs the strip coordinate ~2.5 times closer to the MC muon in comparison with the standard approach;
The optimization of the algorithm needs to be done:
  Time consumption;
  Number of overlapped signals to search selection;
  Initial parameters approximation.
Implementation into CMSSW and testing on various datasets;
Two-track resolution estimation for the new approach.

## Slide 33: ME11 a/b transition region

## Slide 34: ME11a/b transition region
Segment occupancy vs. radius
R(cm)

## Slide 35: Solutions
Segment occupancy vs. radius
R(cm)
~10% increase
Solution : Pass the combined ME11 a + b RecHit collection to the segment builder instead of two separate collections.
No RHs in ME11a/b
RHs only in ME11a
RHs only in ME11b
RHs in ME11 a & b
MC SingleMuPt1000GeV data
Need to look into trigger objects to understand bins № 2 & 3

## Slide 36: Thank you for your attention!

## Slide 37: Back up slides

## Slide 38: Optimal point rejection vs. LSQ 6p->4p
_6p_seg = 273;
_LSQ_seg = 175;
_optimal_point_rej_seg = 0.002;

## Slide 39: Optimal point rejection vs. LSQ 6p->5p
Chart: 
| 1 | 2 | 3 | 4 | 5 | 6
Full segment | 3.7441 | 3.7435 | 3.7435 | 3.7473 | 3.7475 | 3.7432
Simulated segment | 3.7443 | 3.7442 | 3.7443 | 3.7443 | 3.7444 | 3.7445
Optimal poin rejection segment | 3.7441 | 3.7435 | 3.7435 | 3.7473 | 3.7432
LSQ segment | 3.7441 | 3.7435 | 3.7435 | 3.7473 | 3.7475
_6p_seg = 235;
_LSQ_seg = 121 ;
_optimal_point_rej_seg = 54;

## Slide 40: High multiplicity example - 44 RecHits in ME21
Standard
0 segments
New
8 segments
Collisions2015 256630:22:28500814
Muon trajectory

## Slide 41: https://indico.cern.ch/event/611558/contributions/2465877/ talk by Cesare Calabria, 17-02-06 MuPOG Meeting